## Slide 1: Building the Foundation of Earthquakes
Presented by
Paul Johnson

## Slide 2: Why study earthquake engineering?
Earthquakes are a devastating natural disaster:
Average of 10,000 people perish annually [2]
Severe economic and infrastructure loss
Extensive recovery timeframe
Sociological impact

## Slide 3: What causes earthquakes?
Rapid release of elastic energy from rock [8]
  Volcanic eruptions [2]
  Collapse of underground infrastructure [2]
  Aftershocks/tremors
  Crust dislocations : Plate Tectonic Theory [2]
    Normal fault : divergent boundary
    Reverse fault : convergent boundary
    Strike-slip fault : transform boundary

## Slide 4
Top: The 15 tectonic plates; Bottom: Plot of earthquake epicenters [2]

## Slide 5
[2]
Moment Magnitude scale: 32x per level

## Slide 6
Direct and indirect effects of earthquakes [2]

## Slide 7
Types of damage to structures [2]

## Slide 8: Structural response characteristics
Stiffness: resistance of deformations, rigidity
Strength: level of reversible (elastic) deformation
Yield Strength: point of exceeding elasticity
Ultimate Strength: point of total yielding
Ductility: durability beyond elastic deformation (plasticity)

## Slide 9: Structural response contributions
[2]
Stiffness: non-structural damage
Strength: repairable structural damage
Ductility: preventing total yielding

## Slide 10: Structural Analysis
  Equivalent lateral-force procedure: Discretization of masses [3]
Modal analysis procedure [7]
  N modes for N-degree freedom
  Natural frequencies of modes
  System response as linear combination
Push-over (static) Analysis: stiffness, strength, ductility [2]
Inelastic Response: adaptive/dynamic push-over

## Slide 11: Floor Displacement Model
Horizontal Spring Mass System
With and without dampening
[3]

## Slide 12: Higher Order substitutions

## Slide 13: HCP undamped: Relative positions
X(t) relates the displacement from the equilibrium position. K is the spring/stiffness/restoring force. M is the mass.

## Slide 14: Coefficient Matrix

## Slide 15: APC Solver
  Every m=10000 kg
  Every k=5000 kg/s2
  Displaced initial positions

## Slide 16: T=20

## Slide 17: T=40

## Slide 18: T=100

## Slide 19: Uniformly increasing restoring force 50% decreases period (*converse for mass*)

## Slide 20: Uniformly decreasing restoring force 50% increases period (*converse for mass*)

## Slide 21: Perturbed Position

## Slide 22: Perturbed stiffness/mass

## Slide 23: HCP damped: Relative velocities (proportional to speed)
Horizontal damped spring-mass visualization [5]

## Slide 24: Coefficient Matrix

## Slide 25: Previous example damped T=20

## Slide 26: T=40

## Slide 27: T=100

## Slide 28: Perturbed T=20

## Slide 29: NON-CP: Now with ground movement
Only the first floor has changed
Vector of forcing terms added

## Slide 30: Floor Displacement

## Slide 31: NON-CP damped: now with ground movement
Visualization of building shear and variable representation [3]

## Slide 32: APC Solver
  Every m=10000 kg
  Every k=5000 kg/s2
  Displaced initial positions & velocities
  Damped

## Slide 33: T=60

## Slide 34: Semi-CP: Relative velocities2

## Slide 35: References
[1] Chopra, A. K., (2009), Dynamics of Stuctures (3rd ed.), New Delhi, India: Pearson
[2] Elnashai, A. S., Sarno, L. D., (2008), Fundamentals of Earthquake Engineering, West Sussex, United Kingdom: Wiley.
[3] Ghosh, S. K., (2003), Seismic Design Using Structural Dynamics (2000 IBC), Country Club Hills, IL: International Code Council.
[4] Kalny, O., (2013), Modal Analysis, available at: https://wiki.csiamerica.com/display/kb/Modal+analysis.
[5] Marchand, R., McDevitt, T. J., (1999), “Learning Differential Equations by Exploring Earthquake Induced Structural Vibrations: A Case Study,” International Journal of Continuing Engineering Education and Life-Long Learning, 6, 477-485.
[6] McKibben, A. M., and Webster, M. D., (2015) Differential Equations with MATLAB, New York: CRC Press.
[7] MIT OpenCourseWare, (2013), “Modal Analysis Orthogonality, Mass Stiffness, Damping Matrix,” available at: https://www.youtube.com/watch?v=OxcCPTc_bXw.
[8] Tarbuck, E. J., (2011), Earth an Introduction to Physical Geology (10th ed.), Upper Saddle River, NJ: Pearson Education.